## Slide 1
Presented by Daniel Khashabi
Joint work with Sebastian Nowozin, Jeremy Jancsary, Andrew W. Fitzgibbon and Bruce Lindbloom
Pattern-independent
Demosaicing;

## Slide 2
Outline
Demosaicing problem
Creating input-output pairs
Our demosaicing model
Experiments

## Slide 3
A simple camera pipeline
Demosaicing
Image correction: 3x3 color transform and Gamma correction (nonlinear)
Camera output (sRGB)
Scene
Optical operations
Color Filter Array (CFA)
Analog/Digital Conversion
Linear Transformations: black-level adjustment and color scaling
Raw Spcae
Mosaiced Linear Space
Demosaiced Linear Space
sRGB Space
Images from: http://pho.to/media/images/digital/digital-techlology.jpg

## Slide 4
Bayer Pattern
Demosaicing
Interpolating color-filter-array (CFA) samples to create full-resolution color images
Isn’t a solved problem?! NO!
The current methods are can be improved in terms of performance
    Zippering effect still present in the output of many current method
The current methods are CFA-specific (mostly Bayer pattern) And not easily generalizable to new CFAs
All method are engineered for sRGB images
  Demosaicing is lacking a good dataset
Many of low-level task could be done before/joint with demosaicing
  Noise behaviour changes after demosaicing
Raw Spcae
Mosaiced Linear Space
Demosaiced Linear Space
sRGB Space
Fuji X-trans
Image from: http://i.i.cbsi.com/cnwk.1d/i/tim/2012/02/06/Adobe-raw-demosaic-diagram.jpg

## Slide 5
Overview of our approach
We design a supervised model.
For training the model we propose a procedure to create the ground truth dataset from light-space images
  Our dataset is will be published with our work.
Our model is easily generalizable to different CFA patterns.
Our model can perform denoising jointly with demosaicing.
Raw Spcae
Mosaiced Linear Space
Demosaiced Linear Space
sRGB Space

## Slide 6
Creating ground-truth images
We want to design set of input-output pairs in linear light-space
We use the fact that images are scale-invariant
  regardless of some properties like noise distribution
Raw Spcae
Mosaiced Linear Space
Demosaiced Linear Space
sRGB Space
Ground truth output image
Ground truth input image
Virtual sensor

## Slide 7
down-scaling strategies
There is a systematic bias between red and blue, when the size of the square is even
When the size of the block is odd, this systematic bias vanishes, but the ratio of color sensors are different
  This ratio goes to one, when the size of the block increases
We devised a strategy to compensate for the systematic bias when the size of the window is even

## Slide 8
Max-Ent down-scaling
Goal:
  Want to bring the center of the mass, for each color, to the center of each block
Uniform
MaxEnt

## Slide 9
Down-scaling, a real example

## Slide 10
Creating ground-truth images
Collected 500 raw images captured by Panasonic-Lumix LX-3
We need to be able to go along a good camera pipeline
We use dcraw to transfer images to different stages in camera pipeline
We write out the specifications of each step, for each image
Then simulate our own pipeline in MATLAB, with demosaicing replaced with our own down-scaling
Demosaicing
Image correction: 3x3 color transform and Gamma correction (nonlinear)
Camera output (sRGB)
Linear Transformations: black-level adjustment and color scaling
Raw images
Down-scaling
Image correction: 3x3 color transform and Gamma correction (nonlinear)
Camera output (sRGB)
Linear Transformations: black-level adjustment and color scaling
Raw images
Ground truth output image

## Slide 11
The noise behaviour in down-scaled images
Averaging decreases the noise present in images.
Need to devise a way to bring back the noise into our images
  Since the goal is to perform demosaicing on the original raw images
We use a recent method of noise estimation for raw images [1]
  Models as Poisson-Gaussian distribution
We then add back the noise into images
[1] Foi, Alessandro, et al. "Practical Poissonian-Gaussian noise modeling and fitting for single-image raw-data." Image Processing, IEEE Transactions on 17.10 (2008): 1737-1754.
Down-scaling
Linear Transformations: black-level adjustment and color scaling
Raw images
Image correction: 3x3 color transform and Gamma correction (nonlinear)
Camera output (sRGB)
Noise estimation
Noise addition

## Slide 12
Samples of noise-addition to image

## Slide 13
Possible tasks
We have developed these images
  Among the above tasks we are mostly interested in doing the followings:
    Demosaicing in linear light-space
    Deniosing +demosaicing in linear light-spcae
Raw images
Noise-free-linear
Noise-free-sRGB
Noisy-linear
Noisy-sRGB
Raw Spcae
Mosaiced Linear Space
Demosaiced Linear Space
sRGB Space

## Slide 14
Regression tree field
Combines regression tress (Non-parametric) and Gaussian Random Fields
Energy defined for each factor:
  Measure of the goodness of particular labelling given inputs, and parameters of the factor
  Coefficients of are determined by the regression tree, or each leave stores set of parameters.
Inference:
Training: Jointly choosing the structure of the tree, and parameters of at leaves such that minimizes the empirical risk, in greedy way:

## Slide 15
Regression tree fields, for demosaicing
Tree Feature checks,
  A preliminary bilinear interpolation
  RFS filters [1] which act like derivatives in different directions, with various scales
Quadratic energy basis vectors,
  Set of neightbouring pixels,
  RFS filter responses
[1] RFS filters: http://www.robots.ox.ac.uk/~vgg/research/texclass/filters.html

## Slide 16
Regression tree fields, for demosaicing
The generalized loss function,
  An approximate camera pipeline, from linear-space, to sRGB space, which is differentiable
    An analytic approximation for gamma transform
    An approximate 3x3 color transform,
Stacking RTFs,
[1] RFS filters: http://www.robots.ox.ac.uk/~vgg/research/texclass/filters.html
Mosaiced image
RTF1
RTF2
Raw Spcae
Mosaiced Linear Space
Demosaiced Linear Space
sRGB Space
2
2

## Slide 17
Experiments(1)
Demosaicing, in linear-space, without noise:

## Slide 18
Experiments(2)
Demosaicing, in linear-space, without noise:

## Slide 19
Some samples
Ground truth Bilinear CS RTF
NAT: Non-Local Adaptive Thresholding:
NLM: Non-Local Means

## Slide 20
Some samples
Ground truth Bilinear CS RTF
NAT: Non-Local Adaptive Thresholding:
NLM: Non-Local Means

## Slide 21
Image Margins
Not a considerable margin in RTF outputs
NAT NLM OneStepAP RTF
NAT: Non-Local Adaptive Thresholding:
NLM: Non-Local Means

## Slide 22
And more to go ….
RTF with the generalized loss function
Full denoising-demosiacing experiments
Other CFA patterns: Fuji-Xtrans pattern
Further work?!